## Slide 1
Spatiotemporal
cnn-rnn proxy model
for co2 monitoring
ExxonMobil visit day
April 26th, 2023
Misael M. Morales
Graduate Research Assistant, The University of Texas at Austin
Michael J. Pyrcz
Professor, The University of Texas at Austin
Carlos Torres-Verdín
Professor, The University of Texas at Austin

## Slide 2
Outline
Well pad 1
Executive Summary
Motivation
CNN-RNN Proxy for CO2 Monitoring
  Reservoir modeling
  Numerical simulation
  Data processing
  Deep learning model
Results
Conclusions & Future Work

## Slide 3
Executive Summary
Well pad 1
Accurate and detailed subsurface models are too large and/or redundant for practical data science applications.
Physics-based forward reservoir simulation is very time consuming and computationally expensive.
We design a forward simulator for CO2 monitoring using a deep learning architecture that exploits the latent space dynamics, while integrating spatial structure (CNN) and temporal structure (RNN).
We recommend to work in latent space for subsurface modeling, characterization, and simulation.

## Slide 4
Motivation
There tends to be a high degree of correlation and structure in 2D/3D subsurface data, which makes it a perfect candidate for latent space analysis and modeling.
Encoder-Recurrent-Decoder architectures allow for efficient latent space representation and forward modeling of subsurface data.
CNN-RNN architecture

## Slide 5
Maldonado-Cruz & Pyrcz, (2022) J Pet. Sci. Eng.:
  U-Net for surrogate flow model under geologic uncertainty
  Generate saturation maps based on different PV injected from the permeability/porosity realizations
Jo, Pan, Santos, Jung & Pyrcz, (2021) J Pet. Sci. Eng.:
  Machine learning-assisted history matching
  Using GAN for automatic history matching of deepwater lobe systems
Alakeely & Horne, (2020) SPE Res. Eval. Eng.:
  Deep learning models for downhole signal predictions
  Comparison of CNN and RNN for the prediction of downhole rates, pressure, choke setting, etc.
Kim & Durlofsky, (2022) ArXiV:
  CNN-RNN for robust optimization and closed-loop management
  CNN-LSTM architecture from to predict production rates from permeability maps
Kaur, Fomel, et. al., (2022) GeoSci World Interpretation:
  Seismic Inversion via CNN-RNN architecture
  Used a CNN-Transformer architecture to predict permeability from seismic response
Recent Literature
We propose a new method for image-to-image forward modeling from static model () to dynamic response (, exploiting spatiotemporal latent space dynamics, applied to CO2 monitoring.
Notes: Recent advances in Deep Learning applications in petroleum engineering and subsurface modeling (as well as seismic reservoir characterization/inversion)
None have developed image-to-image (or image-to-timelapse images) deep learning proxy!

## Slide 6
Develop a deep learning framework for forward reservoir simulation of CO2 migration.
Exploit latent space dynamics for timelapse predictions using a CNN-RNN architecture.
Proposed workflow is separated in four parts:
Motivation
2. Numerical Simulation
(MRST)
1. Reservoir Model
(SPE10)
3. Data Processing
(Python)
4. Deep Learning
(Keras)
Notes: This project is composed of 4 main parts (reservoir model, numerical simulation, data processing, and the deep learning-based proxy model
The proxy model is CNN-RNN-CNN encoder-decoder structure that exploits latent space dynamics to model a timelapse of saturation from a static permeability input.

## Slide 7
Classical numerical reservoir simulator workflow (data generation):
  Load SPE10 model static properties
  Partition grid from 3D to unique 2D maps.
  Use two-phase water-gas solver to find states over time.
Reservoir Modeling
SPE10 model
partition
grid
reservoir
simulation
Timelapse saturation states
Simulator inputs
Tarbert (Gaussian) + Ness (fluvial)
Pros: accepted as ground truth (accurate)
Cons: computationally expensive
CNN-RNN Proxy
Notes: Data comes from SPE10
We partition the 220x60x85 model into 255 x (60,60) realizations and use MRST to forward-simulate CO2 injection. We collect 60 saturation states (60 months) for each realization

## Slide 8
High-fidelity simulations are performed using MRST CO2 Lab.
  Two-phase water-gas model
  Output: dynamic pressure & saturation fields
255, 2D realizations with 1 injector:
  Initially water saturated
  CO2 injection @ 5 m3/day
  5 years, monitored monthly
  Automatic Differentiation framework
Parallelized over 10 cores on an Intel i9-10900K @ 5000 MHz.
  seconds per realization
CO2-Brine relative perm curves
MRST simulator code
HFS input and outputs
Numerical Simulation
Notes: Numerical simulation is done using MRST (in parallel)
CO2Lab module in MRST provides a simplified model for CO2 injection. We use most of the default parameters for CO2 properties
Inject for 5 years, monitored monthly (60 states)
Inject 5 m^3 per day
One injector in the center

## Slide 9
HFS sliced into:
and
Reshape to:
and
Data augmentation:
rotation realizations
Shuffle concatenated dataset:
  Make proxy agnostic to orientation
  Learn true flow physics
Min-Max Normalization:
Train (66%), Test (33%) random split
Augmented permeability & saturation data
Train/Test distribution for mean input & output
Data Processing
Notes: Data from MRST is then pre-processed in order to have better machine learning
6 preprocessing steps

## Slide 10
Encoder-recurrent-decoder architecture to predict dynamic saturation states from permeability
unfold
Folded CNN-RNN architecture
Unfolded CNN-RNN architecture
CNN-RNN Proxy
Notes: Schematic of the CNN-RNN model
Left = “Folded” model, where we clearly see the encoder-recurrent-decoder architecture
Right = “Unfolded” model, where we can visualize the latent space dynamics, meaning that the latent vector is expanded into 125 features (5,5,5), and updated according to the saturation map (60,60,60)

## Slide 11
Conv2D
Conv2D
BatchNorm
LeakyReLU
MaxPool2D
regularization
LeakyReLU activation
Convolutional block
Conv Block 1
Conv Block 2
Conv Block 3
Conv Block 4
The Encoder
Overall
CNN-RNN
architecture
CNN-RNN Proxy
Notes: Encoder section
Contains 4 convolutional blocks
Each convolutional block has Conv2D(LeakyRelu)-Conv2D(l2norm)-BatchNorm-LeakyReLu-MaxPool --- the pooling reduces dimensions

## Slide 12
RepeatVector
Reshape
Flatten
GRU
Flatten
RepeatVector
GRU
Reshape
Recurrent block
Overall
CNN-RNN
architecture
The Recurrent Block
CNN-RNN Proxy
Notes: Recurrent section
We flatten the latent space, Z (576)
Repeat it 125 times
Apply recurrent layer (GRU, many-to-many) such that (125,576)->(125,128)
Reshape into (5,5,5128) … (length, width, height, channels)

## Slide 13
ConvT Block 1
ConvT Block 2
ConvT Block 3
Output Block
ConvT3D
ConvT3D
BatchNorm
LeakyReLU
regularization
LeakyReLU activation
Transpose Convolutional block
ConvT3D
The Decoder
CNN-RNN Proxy
Overall
CNN-RNN
architecture
Notes: Decoder section
Contains 3 Transpose-Convolutional blocks, and an Output block
Each transpose convolutional block has ConvT3D(LeakyRelu)-ConvT3D(LeakyRelu)-ConvT3D(l2norm)-BatchNorm-LeakyReLu ---- the strides increase dimensions

## Slide 14
Compile:
  Optimizer = Nadam (Adam with Nesterov Momentum)
    SSIM: perceptual information comparison based on luminance, contrast, and proximity 
    MSE: pixel-wise comparison based on intensity and location.
Fit:
  Epochs = 300
  Batch Size = 40
  Validation split = 0.25
17 minutes on Nvidia RTX 3080
CNN-RNN Training process
CNN-RNN Proxy
Nadam optimizer formulation
Notes: We then compile and fit the model
We use Nadam, Nesterov Adam. A slight update in the momentum calculation. Works better than Adam for this problem (very small learning rate)
Use a Loss function that combines MSE (pixel-wise) and SSIM (overall image)
SSIM ~ luminance, contrast, perceptual information
Overfit! 

## Slide 15
Training: MSE=0.016 | SSIM=0.867
Training samples
Training inputs
Training predictions
CNN-RNN Proxy
Notes: Training predictions
Very good!

## Slide 16
Testing: MSE=0.040 | SSIM=0.653
Testing samples
Testing inputs
Testing predictions
CNN-RNN Proxy
Notes: Testing Predictions
Not so good, but still useful. Can be improved!

## Slide 17
High-fidelity simulations are the most expensive step.
  20 seconds per realization
Data processing is essential for proper model training.
RNN-CNN:
  930,000 parameters
  Custom MSE-SSIM loss function
  Training requires 17 minutes
  Predictions require 0.5 milliseconds per realization
    40,000 speedup
  Training: 86% & Testing: 65% SSIM
Conclusions
Numerical Simulation
(MRST)
Reservoir Model
(SPE10)
Data Processing
(Python)
Deep Learning
(Keras)
Notes: Significant speedup in the forward simulation
Architecture can be used for other applications

## Slide 18
Subsurface data must be treated in reduced-dimensional space for efficiency, at little or no loss of detail.
Convolutional layers are efficient for dimensionality reduction and data reconstruction.
Recurrent layers serve as simulation time-stepping in latent space.
We recommend to work in reduced-dimensional space when dealing with subsurface models and data, and to use deep learning-based proxy models for computational efficiency.
Conclusions

## Slide 19
Utilize Keras’ TimeDistributed layer for equal-filtering Decoder block.
Extend to 3D
Apply model to other subsurface flow problems:
  Groundwater flow
  Contaminant transport
  Geothermal flows
  Hydrocarbon production
Modify model for:
  Uncertainty quantification
  Inverse modeling
  History matching / model calibration
  Closed-loop / Robust optimization
Future Work
CNN-RNN for latent-space history matching
CNN-RNN for inverse modeling

## Slide 20
References
Maldonado-Cruz, Eduardo, and Michael J Pyrcz. (2022) “Fast Evaluation of Pressure and Saturation Predictions with a Deep Learning Surrogate Flow Model.” Journal of petroleum science & engineering 212
Kim, Y. D., & Durlofsky, L. J. (2022). "Convolutional-Recurrent Neural Network Proxy for Robust Optimization and Closed-Loop Reservoir Management." arXiv preprint arXiv:2203.07524.
Kaur, Harpreet et al. (2022) “Time-Lapse Seismic Data Inversion for Estimating Reservoir Parameters Using Deep Learning.” Interpretation (Tulsa) 10.1
S. Pan, S.L. Brunton, and J.N. Kutz (2022) "Neural Implicit Flow: a mesh-agnostic dimensionality reduction paradigm of spatio-temporal data." arXiv preprint arXiv:2204.03216
Joon, Shams, Dawuda, Ismael, Morgan, Eugene, and Sanjay Srinivasan. (2022) "Rock Physics-Based Data Assimilation of Integrated Continuous Active-Source Seismic and Pressure Monitoring Data during Geological Carbon Storage." SPE Journal.
Gonzalez, Keyla, and Siddharth Misra. (2022) “Unsupervised Learning Monitors the Carbon-Dioxide Plume in the Subsurface Carbon Storage Reservoir.” Expert systems with applications 201
K.G. Gurjao, E. Gildin, R. Gibson, and M. Everett. (2022) "Estimation of Far-Field Fiber Optics Distributed Acoustic Sensing DAS Response Using Spatio-Temporal Machine Learning Schemes and Improvement of Hydraulic Fracture Geometric Characterization." SPE Hydraulic Fracturing Technology Conference and Exhibition, USA
Salazar, Jose J et al. (2022) “Fair Train-Test Split in Machine Learning: Mitigating Spatial Autocorrelation for Improved Prediction Accuracy.” Journal of petroleum science & engineering 209:109885–.
Tang, Meng, Yimin Liu, and Louis J Durlofsky. (2021) “Deep-Learning-Based Surrogate Flow Modeling and Geological Parameterization for Data Assimilation in 3D Subsurface Flow.” Computer methods in applied mechanics and engineering 376:113636–.
H. Jo, Y. Cho, M.J. Pyrcz, H. Tang, and P. Fu (2021) "Machine learning-based porosity estimation from spectral decomposed siesmic data." arXiv preprint arXiv:2111.13581
Wen, Gege, Catherine Hay, and Sally M Benson. (2021) “CCSNet: A Deep Learning Modeling Suite for CO2 Storage.” Advances in water resources 155:104009–.
Alsulaimani, Thamer , and Mary Wheeler. (2021) "Reduced-Order Modeling for Multiphase Flow Using a Physics-Based Deep Learning." SPE Reservoir Simulation Conference
E.J.R. Coutinho, M.J. Aqua and E. Gildin. (2021) "Physics-Aware Deep-Learning-Based Proxy Reservoir Simulation Model Equipped with State and Well Output Prediction." SPE Reservoir Simulation Conference, Virtual.
Ciriello, V., Lee, J. & Tartakovsky, D.M. (2021) "Advances in uncertainty quantification for water resources applications." Stoch Environ Res Risk Assess 35, 955–957
Pan, W., Torres-Verdín, C. & Pyrcz, M.J. (2021) "Stochastic Pix2pix: A New Machine Learning Method for Geophysical and Well Conditioning of Rule-Based Channel Reservoir Models." Nat Resour Res 30, 1319–1345
Wu, Hao et al. (2021) “A Multi-Dimensional Parametric Study of Variability in Multi-Phase Flow Dynamics During Geologic CO2 Sequestration Accelerated with Machine Learning.” Applied energy 287:116580–.
Santos, J.E., Yin, Y., Jo, H. et al. (2021) "Computationally Efficient Multiscale Neural Networks Applied to Fluid Flow in Complex 3D Porous Media." Transp Porous Med 140, 241–272
Chan, S., Elsheikh, A.H. (2020) "Data-driven acceleration of multiscale methods for uncertainty quantification: application in transient multiphase flow in porous media." Int J Geomath 11,3
Cheung, S.W., Chung, E.T., Efendiev, Y. et al. (2020) "Deep global model reduction learning in porous media flow simulation." Comput Geosci 24, 261–274
Almasov, Azad , Onur, Mustafa , and Albert C. Reynolds. (2020) "Production Optimization of the CO2 Huff-N-Puff Process in an Unconventional Reservoir Using a Machine Learning Based Proxy." SPE Improved Oil Recovery Conference, Virtual
Jiang, Chiyu lmaxr et al. (2020) “MESHFREEFLOWNET: A Physics-Constrained Deep Continuous Space-Time Super-Resolution Framework.” SC20: International Conference for High Performance Computing, Networking, Storage and Analysis. IEEE 1–15.
J. Nagoor Kani, Elsheikh, A.H. (2019) "Reduced-Order Modeling of Subsurface Multi-phase Flow Models Using Deep Residual Recurrent Neural Networks." Transp Porous Med 126, 713–741
Jayne, Richard S, Hao Wu, and Ryan M Pollyea. (2019) “Geologic CO2 Sequestration and Permeability Uncertainty in a Highly Heterogeneous Reservoir.” International journal of greenhouse gas control 83.C:128–139.
K.-A. Lie. (2019) "An Introduction to Reservoir Simulation Using MATLAB/GNU Octave: User Guide for the MATLAB Reservoir Simulation Toolbox (MRST)." Cambridge University Press
Brunton, Steven L., and Jose Nathan Kutz. (2019) "Data-Driven Science and Engineering: Machine Learning, Dynamical Systems, and Control." 1st ed. Cambridge University Press
Guo, Zhenyu, and Albert C Reynolds. (2018) “Robust Life-Cycle Production Optimization With a Support-Vector-Regression Proxy.” SPE journal 23.6:2409–2427
Naraghi, Morteza Elahi, Spikes, Kyle , and Sanjay Srinivasan. (2017) "3D Reconstruction of Porous Media From a 2D Section and Comparisons of Transport and Elastic Properties." SPE Res Eval & Eng 20:342–352
Ampomah, W et al. (2017) “Optimum Design of CO2 Storage and Oil Recovery Under Geological Uncertainty.” Applied energy 195
J. Nagoor Kani, Elsheikh, A.H. (2017) "DR-RNN: A deep residual recurrent neural network for model reduction." arXiv preprint arXiv:1709.00939

## Slide 21
Acknowledgments
Appreciation for the support from the DIRECT member companies.
Well pad 1

## Slide 22
Thank You
Q & A
ExxonMobil visit day
April 26th, 2023
Misael M. Morales
Graduate Research Assistant, The University of Texas at Austin
Michael J. Pyrcz
Professor, The University of Texas at Austin
Carlos Torres-Verdín
Professor, The University of Texas at Austin

## Slide 23
MSE and SSIM formulas:
A perceptual information comparison including luminance, contrast, and proximity
A pixel-wise comparison based on intensity and location
is the original data matrix and are the dimensions ()
is the reconstructed data matrix and are stability constants

## Slide 24
Simulation Variables
Reference pressure: mega Pascals
Reference temperature:
Water compressibility:
Rock compressibility: bars
Water viscosity: Pascal-second
CO2 viscosity: Pascal-second
Residual water saturation:
Residual CO2 saturation:
Water viscosity: 1000
Grid size: 60x60x1
Grid dimensions: 20x10x5 ft
Initial reservoir pressure: psia
Initial reservoir saturation: -
Total simulation time: 5 years
Monitor steps: 1 month
Total steps: 60
Wellbore radius: 0.05
AD Solver: TwoPhaseWaterGasModel

## Slide 25
Proxy Model Variables
L2 regularization: 1e-4
LeakyReLU alpha: 0.3
RNN dropout: 0.2
Nadam learning rate: 5e-4